## Slide 1: Soft Processor Design
Lucas Donovan

## Slide 2: System Overview
Zedboard
Inputs
  8 switches
  3 buttons
  System Clock
Outputs
  8 LEDs
  Pmod seven segment display module (2 digits)

## Slide 3: Registers
Program Counter (4 bits)
Accumulator (4 bits)
Instruction Register (8 bits)
General Purpose Registers (16 x 4 bits)
reg [3:0] R [0:15];
2 Condition Codes (1 bit each)
  Zero
  Carry

## Slide 4: Instruction Set
Format
16 total opcodes
6 register direct instructions
3 immediate instructions
5 branching instructions
ROM mode
Halt instruction

## Slide 5: ROM Mode
When the opcode is 0, the processor executes the instructions in the ROM.
ROM input is the PC, output is the instruction to run.
module Instruction_ROM (
input [3:0] pc,
output reg [7:0] instr
);

## Slide 6: Example Program - Counter
0001_0000; // LOD 0 - ACC = R0
1000_0001; // ADI 1 - ACC = ACC + 1
0010_0000; // STR 0 - R0 = ACC
1011_0000; // JNZ 0 - PC = 0
if ACC != 0
1111_1111; // HLT F - Halt Execution
The first instruction isn’t necessary, but it when removed the program will reset completely even if the registers aren’t reset, whereas with it will keep it’s value.

## Slide 7: Demonstration